## Slide 1
Anomaly Detection in Wind Turbines
A comparative study using SCADA time-series data and deep learning
DATASET
CARE_To_Compare · Wind Farm C
MODELS
CNN · LSTM · CNN-LSTM · Autoencoders
AUTHOR & DATE
Thiago Heleno · April 2026

## Slide 2
Overview
The Research Question
Can deep learning automatically detect mechanical anomalies in wind turbines from raw SCADA sensor readings — and which paradigm performs better under severe class imbalance?
SUPERVISED- Based on a Chinese paper
Notebook 1 · CNN-LSTM
The model learns the difference between Normal and Anomaly from labeled examples. Requires annotated fault data. Output: binary label.
SEMI-SUPERVISED – Nb3 based on the CARE Score
Notebooks 2 & 3 · Autoencoders
The model learns only what normal looks like. Anomalies are deviations — detected via reconstruction error.
Why this matters
Wind turbines are expensive to maintain and hard to access offshore
Early fault detection reduces downtime and repair costs significantly
SCADA data is abundant but anomaly labels are rare and expensive
Class imbalance (98% normal / 2% anomaly) is the central technical challenge
Core question: does semi-supervised anomaly detection outperform supervised classification when fault labels are scarce and data is heavily imbalanced?

## Slide 3
Data
The Dataset — CARE_To_Compare Wind Farm C
3.18M
Total rows
238
Physical sensors
58
Recorded events
10 min
Sampling interval
Sensor Columns After Preprocessing
238 physical sensors x 4 statistics (avg, min, max, std) = 952 raw SCADA columns. Sin/cos encoding is applied as a separate preprocessing step for angular features — preserving circular continuity where 359 deg is close to 1 deg.
Event Composition
Type | NB1 / NB2 | NB3 (Keras)
Anomaly events | 27 | 27
Normal events | 31 | 31
Class Imbalance — The Central Challenge
Normal 98.1%
Class | Samples | Share
Normal | 3,126,239 | 98.1%
Anomaly | 60,897 | 1.9%
Imbalance ratio: 51:1. A model that always predicts "Normal" reaches 98% accuracy while detecting zero faults. Accuracy is therefore meaningless here.

## Slide 4
Data
Train / Validation / Test Splits
NB1
Split by Event
Partitioned at event boundaries — no temporal overlap between splits.
Split | Events | Anomaly | Normal
Train | 40 | 18 | 22
Validation | 8 | 4 | 4
Test | 10 | 5 | 5
After windowing + undersampling: Train 50K normal + 50K anomaly (1:1). Test: 532K normal + 9K anomaly (58:1 real ratio).
NB2 & NB3 — SEMI-SUPERVISED
Temporal Split — 70 / 15 / 15
Chronological partition respecting time ordering of readings.
TRAIN 70% · 2.23M rows
VAL
TEST
Anti-leakage rule: MinMaxScaler is fitted only on normal training samples — never on validation, test, or anomaly data.
Autoencoder training: only normal windows are presented during training. The model never sees a labeled anomaly.

## Slide 5
Data
Preprocessing Pipeline
STEPS APPLIED ACROSS ALL NOTEBOOKS
1
Load 58 event CSV files from Wind Farm C
2
DataClipper — clips extreme outliers to Q0.1% and Q99.9% per feature
3
DuplicateValuesToNaN — sensors frozen for 6+ consecutive readings become NaN
4
SimpleImputer — forward-fill → backward-fill → fill zeros
5
Angle encoding (NB2/3) — each angular sensor → sin + cos pair; 238 sensors → 952 columns
6
MinMaxScaler [0,1] — fitted exclusively on normal training data
7
Feature selection → 285 features (NB1) or 305 features (NB2/3)
Why freeze/outlier detection?
Industrial SCADA hardware can freeze or spike due to communication errors. These are data quality issues, not physical anomalies, and must be removed before modelling.
Why sin/cos for angles?
Raw: 359° ↔ 1° = 358 apart (wrong!). sin/cos encoding: ≈ identical vectors ✓. Preserves circular geometry that ML models need to generalise.
Why scale only on normal data?
If anomaly values influence the scaler's range, their out-of-distribution signals are compressed. Fitting only on normal data preserves anomaly extremes after scaling.

## Slide 6
Data
Feature Selection — 952 → ~300 Features
NB1 — Supervised (XGBoost)
952 raw features
952
↓ Train XGBoost on 100K sampled rows, rank by feature gain. Keep top 30%.
285 final features
285
✓ Selects features most discriminative between Normal and Anomaly
✗ Requires labels — unusable without annotated fault data
NB2 & NB3 — Unsupervised Filtering
952 raw features
952
↓ Remove variance < 0.0001 (nearly constant) → −46
906 remain
906
↓ Remove correlation with operational vars < 0.1 → −129
777 remain
777
↓ Remove inter-feature correlation > 0.95 → −472
305 final features
305
Operational reference variables: power output, wind speed, sensor_144/145 (avg/max/min/std).

## Slide 7
Models
Three Modelling Approaches
NOTEBOOK 1
CNN / LSTM / CNN-LSTM
Paradigm | Supervised
Framework | PyTorch
Input | 36 × 285 (window)
Output | Binary label 0/1
Loss | CrossEntropy
Balancing | Undersampling 1:1
Parameters | ~160K
NOTEBOOK 2
CNN-BiLSTM Autoencoder
Paradigm | Semi-supervised
Framework | PyTorch
Input | 36 × 305 (window)
Output | Reconstruct input
Loss | MAE
Balancing | N/A — normal only
Parameters | ~954K
NOTEBOOK 3
Keras MLP Autoencoder
Paradigm | Semi-supervised
Framework | TF / Keras
Input | 305 (single sample)
Output | Reconstruct input
Loss | MSE
Balancing | N/A — normal only
Parameters | ~150K
Fundamental difference: NB1 is told "this is what a fault looks like." NB2 and NB3 are told "this is what healthy operation looks like — flag anything else." NB3 operates pointwise (no temporal context); NB2 operates over 6-hour windows.

## Slide 8
Notebook 1
CNN-LSTM — Supervised Pipeline
1
Load 58 CSVs → split by event (no window overlap across splits)
2
MinMaxScaler fitted on normal train data only → normalize [0, 1]
3
XGBoost feature selection on 100K sample → top 30% = 285 features
4
Sliding windows of 36 timesteps (6 hours) — label = Anomaly if any step is anomalous
5
Undersampling (train only) — keep 2.3% of normal windows → balanced 1:1 training set
6
Train CNN, LSTM, and CNN-LSTM with CrossEntropy loss · Adam · up to 500 epochs
7
Sweep thresholds on validation → choose threshold maximising F1-Score
8
Apply optimal threshold to test set (natural 58:1 ratio) → final metrics
Window Labelling Strategy
[ N N N N N N N N ] → 0 (Normal)
[ N N A N N N N N ] → 1 (Anomaly)
# ANY anomaly in window → label = 1
Training Configuration
Optimizer | Adam (lr = 0.001)
Batch size | 600
Max epochs | 500
Early stopping | patience = 20 (val_loss)
Device | GPU (CUDA)
Loss | CrossEntropyLoss

## Slide 9
Notebook 1
CNN, LSTM, and CNN-LSTM Architectures
Convolutional Network
Input (B, 36, 285)
↓ Transpose → (B, 285, 36)
Conv1D(285→32, k=3) + SELU
↓ MaxPool(k=2)
Conv1D(32→64, k=2) + SELU
↓ MaxPool(k=3) → (B,64,5)
Flatten → (B, 320)
↓ AlphaDropout(0.5)
Dense 320→50 + SELU
Dense 50→10 + SELU
Dense 10→2 + Softmax
Recurrent Network
Input (B, 36, 285)
↓
LSTM(285→100)
↓
LSTM(100→80)
↓ last timestep → (B, 80)
Dropout(0.5)
Dense 80→50 + SELU
Dense 50→10 + SELU
Dense 10→2 + Softmax
Hybrid CNN-LSTM (best)
Input (B, 36, 285)
↓ Transpose
Conv1D(285→32) + SELU
↓ MaxPool → (B,32,17)
Conv1D(32→64) + SELU
↓ MaxPool → (B,5,64)
LSTM(64→100)
LSTM(100→80)
↓ last step → (B, 80)
Dense 80→50→10 + SELU
Dense 10→2 + Softmax
CNN-LSTM: convolutions compress 36 timesteps → 5, then LSTM learns temporal dependencies on the reduced sequence. AlphaDropout preserves SELU's self-normalising property.

## Slide 10
Notebook 2
CNN-BiLSTM Autoencoder — Semi-supervised Pipeline
1
Temporal split 70/15/15 — preserves chronological ordering
2
Preprocessing: DataClipper → DuplicateToNaN → Imputation → MinMaxScaler
3
Unsupervised feature selection → 305 features
4
Sliding windows of 36 timesteps — train and val use only normal windows
5
Train CNN-BiLSTM-Attention Autoencoder — MAE loss, mixed precision (AMP), 100 epochs
6
Compute per-feature thresholds (P95 and P99) on normal validation windows
7
Anomaly if ≥ 15 of 305 features exceed their individual threshold
8
v4 post-hoc refinements — feature weighting, temporal smoothing, informative mask
The Autoencoder Principle
Normal → Encoder → Latent → Decoder → ≈ Input (low reconstruction error)
Anomaly → Encoder → Latent → Decoder → ≠ Input (high reconstruction error → flag!)
Detection
If in the 5 windows before, there are more anomalies than normal, it flags a real anomaly in the window

## Slide 11
Notebook 2
CNN-BiLSTM-Attention Architecture · ~954K Parameters
ENCODER
Input: (B, 36, 305) — 6-hour window × 305 features
↓
Conv1D(305→64, k=3, pad=1) + SELU → (B, 36, 64)
↓ captures local temporal patterns
Conv1D(64→128, k=3, pad=1) + SELU → (B, 36, 128)
↓
BiLSTM(128 → 256 bidirectional) → (B, 36, 256)
↓ past + future context simultaneously
BiLSTM(256 → 128 bidirectional) → (B, 36, 128)
↓
MultiHeadAttention(embed=128, heads=4) + LayerNorm → (B, 36, 128)
DECODER
Latent: (B, 36, 128)
↓
LSTM(128→128) + SELU → (B, 36, 128)
↓
LSTM(128→128) + SELU → (B, 36, 128)
↓ Dropout(0.15)
Linear(128→256) + SELU → (B, 36, 256)
↓
Linear(256→305) → Reconstruction (B, 36, 305)
BiLSTM processes the sequence in both directions, capturing richer temporal dependencies. Multi-Head Attention learns which timesteps and features contribute most to reconstruction quality.

## Slide 12
Notebook 3
Keras MLP Autoencoder + Optuna
1
Temporal split 70/15/15 — cut points: Oct 2025 and May 2027
2
sklearn Pipeline: DataClipper → DuplicateToNaN → Imputation → MinMaxScaler
3
Unsupervised feature selection → 305 features (same strategy as NB2)
4
Optuna Study 1 (50 trials) — architecture hyperparameter search
5
Optuna Study 2 (50 trials) — adaptive threshold gamma search
6
Train final MLP autoencoder — MSE loss, 50 epochs, ExponentialDecay LR
7
Adaptive threshold: threshold(xi) = RMSE_predicted(xi) + gamma
8
Evaluate with CARE metric — per-event and per-sample scoring
Optuna Hyperparameter Search
Parameter | Range | Best
n_layers | [1, 2, 3] | 2
code_size | [10, 100] | 35
learning_rate | [1e-4, 1e-2] | 9.795e-4
decay_rate | [0.90, 0.999] | 0.9941
gamma | [0.0, 0.5] | 0.4997
Adaptive Threshold
threshold(xi) = RMSE_predicted(xi) + gamma
Detection
“screenshots” a timestep and tries to reconstruct, if the reconstruction error is over the threshold, mark as a temporary anomaly. If the next 6 timesteps are anomaly, the event is marked as an anomaly

## Slide 13
Notebook 3
Dense MLP Architecture ~150K Parameters
ENCODER
Input: (B, 305)
v
Dense(305->200) + PReLU
v
Dense(200->100) + PReLU
v
Bottleneck Dense(100->35) + PReLU
DECODER
Latent: (B, 35)
v
Dense(35->100) + PReLU
v
Dense(100->200) + PReLU
v
Dense(200->305) linear
Pointwise vs. Windowed Processing
 | NB2 (BiLSTM) | NB3 (MLP)
Temporal context | 36 timesteps (6h) | None
Input shape | (B, 36, 305) | (B, 305)
Captures trends | Yes | No
Computational cost | High | Low
PReLU Activation
PReLU(x) = max(0,x) + alpha*min(0,x) <- alpha is learned
Unlike standard ReLU (alpha=0 fixed), the negative slope is a trained parameter allowing more flexibility in representing asymmetric sensor distributions.
Bottleneck of 35 neurons forces the encoder to compress 305 features into an essential representation of healthy operation. Anything that cannot be faithfully reconstructed is treated as anomalous.

## Slide 14
Evaluation
Metrics — What We Measure and Why
CONFUSION MATRIX
Predicted Normal
Predicted Anomaly
Actual Normal
Actual Anomaly
TN
True Negative
FP
False Alarm
FN
Missed fault!
TP
Detected!
A model predicting "Normal" always achieves 98% accuracy with zero fault detection. Accuracy is unreliable — AUC-ROC and F1 are used instead.
Sample-level vs. Event-level
Per sample — every 10-min reading evaluated. Strict: model must be correct at each timestep.
Per event — event detected if any sample is flagged. "Did we catch this failure?"
METRIC DEFINITIONS
Metric | Formula | Best use
Precision | TP / (TP+FP) | % of alarms that are real faults
Recall | TP / (TP+FN) | % of faults successfully detected
F1-Score | 2*P*R / (P+R) | Harmonic balance of P and R
AUC-ROC | Area under ROC | Threshold-independent ranking
CARE Score | Composite | CARE = (F1_2_mean + WS_mean + EF1_2 + 2.0 * Acc_mean) / 5.0
AUC-ROC = 0.5: no better than random
AUC-ROC = 1.0: perfect separation
AUC-ROC < 0.5: worse than random (e.g. LSTM)
AUC-ROC measures whether the model ranks anomalies above normal samples regardless of threshold — the most honest metric for imbalanced data.

## Slide 15
Results
Sample-Level Performance
Chart: AUC-ROC by Model
| CNN (NB1) | LSTM (NB1) | CNN-LSTM (NB1) | BiLSTM AE (NB2) | Keras MLP (NB3)
AUC-ROC | 0.55 | 0.4 | 0.66 | 0.865 | 0.872
Chart: F1-Score (%) by Model
| CNN (NB1) | LSTM (NB1) | CNN-LSTM (NB1) | BiLSTM AE (NB2) | Keras MLP (NB3)
F1-Score (%) | 5.47 | 0 | 3.16 | 5.78 | 4.52
0.55
CNN - AUC-ROC
0.40
LSTM - AUC-ROC (worse than random)
0.66
CNN-LSTM - AUC-ROC
0.865
BiLSTM AE - AUC-ROC
0.872
Keras MLP AE - AUC-ROC

## Slide 16
Results
Full Results — Sample-Level and Event-Level
SAMPLE-LEVEL METRICS (test set)
Model | Precision | Recall | F1 | AUC-ROC
NB1 CNN | 19.62% | 3.18% | 5.47% | 0.55
NB1 LSTM | 0.00% | 0.00% | 0.00% | 0.40
NB1 CNN-LSTM | 3.28% | 3.05% | 3.16% | 0.66
NB2 P99 | 2.99% | 88.46% | 5.78% | 0.865
NB3 Keras MLP | 2.32% | 88.26% | 4.52% | 0.872
Precision of ~2-3% across all models: the dominant challenge remains excessive false alarms from normal operational variability.
NB2 — EVENT DETECTION (P95 threshold)
Event | Anomalous Windows | Detected | Rate
Event 16 | 2,195 | 2,109 | 96.1%
Event 30 | 3,298 | 3,153 | 95.6%
Event 66 | 978 | 978 | 100.0%
Weighted avg. | - | - | 96.4%
NB3 — CARE SCORE (58 events)
0.699
CARE Score
94.1%
Recall (events) 48 of 51 detected
88.9%
Precision (events) 48 of 54 alarms correct
Event-level evaluation is operationally superior: a fault event spans thousands of timesteps, so detecting even one correctly flags the whole event. This is what matters for maintenance decisions.

## Slide 17
Conclusions
Summary and Model Ranking
1
NB3 — Keras MLP Autoencoder
AUC-ROC 0.872 · CARE 0.699 · Event Recall 94.1% · Precision 88.9%
2
NB2 — CNN-BiLSTM Autoencoder
AUC-ROC 0.865 · Event Recall 96.4% across 3 test events
3
NB1 — CNN-LSTM (best supervised)
AUC-ROC 0.66 · F1 3.16% · LSTM alone: 0% across all metrics
v
Semi-supervised outperforms supervised under severe imbalance — AUC-ROC 0.87 vs 0.66 maximum
x
Isolated LSTM fails completely when train/test balance differs
!
Low Precision (~2-3%) is the main open problem — too many false alarms
v
Event-level evaluation is more operationally meaningful than sample-level

## Slide 18
Future Work
Next Steps
Fix the high amount of False positives Induce failure in the dataset using noise:
Classifier: train the model labelling this new Induced Anomaly
Autoencoder: train the model with Normal data and check the reconstruction error for detecting the Induced Anomalies

## Slide 19
Thank you
Wind Turbine Anomaly Detection IC 2026
DATASET
CARE_To_Compare Wind Farm C
BEST RESULT
AUC-ROC 0.872 Event Recall 94.1%
AUTHOR
Thiago Heleno April 2026
Based on: wind_turbine_cnn_lstm_paper.ipynb wind_turbine_anomaly_detection_v4.ipynb wind_turbine_autoencoder_keras_pipeline.ipynb